## Slide 1
SimCXL • BTP results • 4 Sep 2026
01
BTP • EXPERIMENTAL RESULTS
What the CXL
results show
Latency, traffic and congestion across four successful workloads
Native context • Key findings • Next experiments
Notes: Scope: four successful simulated smoke workloads, three native five-repetition campaigns and exploratory native pilot runs. The deck is a descriptive comparison, not a causal CXL benchmark. All proposals are untested hypotheses.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 2
Inputs differ before memory is compared
Four successful simulator runs; one smoke repetition each. Native campaigns have five repetitions.
SimCXL • BTP results • 4 Sep 2026
02
Workload
Native
SimCXL
Pilot
512 MiB; 8 passes
1 MiB; 8 passes
STREAM
1.2 GB; 20 iterations
1.5 MiB; 3 iterations
Pointer chase
512 MiB; 5 samples
2 MiB; 1 sample
ANN
200k vectors; 1k queries
1,024 vectors; 8 queries
Native: i7-12700, 25 MiB L3 | Sim: 1 TimingSimpleCPU, 96 MiB L3
Notes: [Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 3
CXL read tails reach about 600 ns
Completed workload phases • Host-facing CXL request to returning response
SimCXL • BTP results • 4 Sep 2026
03
Chart: Latency (ns)
| Pilot | STREAM | Pointer | ANN
Mean | 301.3321 | 296.8218 | 300.4013 | 290.0494
P95 | 442.437 | 406.158 | 424.089 | 397.761
P99 | 631.338 | 597.545 | 605.484 | 607.569
290–301 ns
Mean read latency is similar across the four runs.
598–631 ns
P99 is approximately twice the mean.
CXL boundary
CPU and cache lookup time is outside this measurement.
Notes: Ticks converted to ns using 1e12 ticks/s. These are transaction distributions, not application runtimes and not CPU-to-memory instruction latencies. One run per workload. P50/P95/P99 are empirical percentiles, not confidence intervals.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 4
The modeled path adds about 165 ns
Mean latency components sum to total • This is not an incremental native-DRAM penalty
SimCXL • BTP results • 4 Sep 2026
04
Chart: Mean latency (ns)
| Pilot | STREAM | Pointer | ANN
Fabric | 68.0432 | 67.563 | 67.8061 | 66.6639
Enqueue→start | 16.3275 | 16.3244 | 16.3269 | 16.3056
Device | 135.6464 | 131.6194 | 134.9534 | 125.7638
Return | 81.3151 | 81.3151 | 81.315 | 81.3161
148–149 ns
Fabric plus return-path time per read.
126–136 ns
Device service, including backend scheduling.
55–57%
Share outside device service; not all avoidable.
Notes: Fabric plus return is 148–149 ns; fabric + enqueue-to-start + return is about 165 ns. Enqueue-to-start contains modeled protocol/scheduling delay, not only congestion. Device service includes backend memory scheduling. No matched local-memory path measurement is present.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 5
Traffic volume reflects different phases
Read payload observed at the CXL boundary • 64 bytes per recorded read
SimCXL • BTP results • 4 Sep 2026
05
Chart: CXL read payload (MiB)
| Pilot | STREAM | Pointer | ANN
Read MiB | 1.2038 | 1.8303 | 67.5866 | 5.7145
67.6 MiB
Pointer chase transfers the most data over its 1.22 s phase.
1.11 million
Pointer read requests; includes process setup activity.
0 write bytes
Recorded in all four phases; write behavior remains untested.
Notes: Transferred bytes are actual CXL payload, not application logical traffic. Unequal phase lengths and initialization costs confound total traffic comparisons. All four have zero recorded writes during the workload phase; stores may remain cached or write back outside it.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 6
Peak traffic exceeds the phase average
Read bandwidth in decimal GB/s • Peaks use fixed 1 ms simulation windows
SimCXL • BTP results • 4 Sep 2026
06
Chart: Read bandwidth (GB/s)
| Pilot | STREAM | Pointer | ANN
Phase mean | 0.072854 | 0.042061 | 0.057972 | 0.016362
1 ms peak | 0.4112 | 0.45466 | 0.50381 | 0.43008
0.016–0.073
Phase-average GB/s. Long quiet intervals dilute averages.
0.411–0.504
Peak GB/s in the recorded windows.
Capacity unknown
These values do not establish a CXL bandwidth ceiling.
Notes: Average = read payload / completed phase seconds / 1e9. Peak is the reporter peak window metric at 1e9 ticks per window and 1e12 ticks per second. Peak is not endpoint capacity; compare equal window definitions. Endpoint read/write capacities were unspecified.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 7
Admission stalls occur in brief bursts
Endpoint queue-full attempts normalized by CXL read requests
SimCXL • BTP results • 4 Sep 2026
07
Chart: Events / 1,000 reads
| Pilot | STREAM | Pointer | ANN
Events per 1,000 reads | 75.1914 | 67.596 | 69.4123 | 41.2915
41–75 events
Per 1,000 reads; not a blocked-request percentage.
P99 depth = 0
Endpoint request queue is empty for at least 99% of phase time.
Max depth = 40
Short bursts still occur despite low time-weighted depth.
Notes: Queue-full event / read requests * 1000. This normalizes raw counts for unequal request volumes but is not a probability of a request being blocked: multiple attempts may belong to one request. Endpoint CXLType2Accel admission can reject due to request or response queue state. Backpressure cycles are node-level, not CPU memory-stall cycles.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 8
Port utilization stays below 0.2%
Upstream crossbar read utilization • Endpoint utilization remains unknown
SimCXL • BTP results • 4 Sep 2026
08
Chart: Modeled port utilization (%)
| Pilot | STREAM | Pointer | ANN
Read utilization (%) | 0.18988 | 0.10962 | 0.15109 | 0.042642
0.043–0.190%
Measured phase-average read utilization.
38.37 GB/s
Denominator from crossbar width and simulated clock.
No ceiling shown
A low average does not rule out brief congestion.
Notes: cxl.link.1.read_utilization * 100. Denominator = 16 bytes / 417 ps = 38.3693 GB/s, modeled crossbar directional payload capacity, not an advertised physical CXL link. All endpoint utilization values are null; do not substitute port utilization. Low averages cannot rule out short bursts.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 9
ANN shows a gap, not a CXL penalty
Queries per second • Native repetitions versus one simulator smoke run
SimCXL • BTP results • 4 Sep 2026
09
Chart: Queries/s
| N1 | N2 | N3 | N4 | N5 | Sim
Queries/s | 72190.7823 | 73021.0883 | 73534.4132 | 72821.5064 | 68628.358 | 2667.0721
72,039 vs 2,667
Native mean versus simulator output.
27× observed gap
Different inputs, CPU model, cache and concurrency.
No attribution
These data do not isolate CXL as the cause.
Notes: Native five QPS values from stdout_core_cache.log only: mean 72039.22964, sample SD 1966.51. All five individually plotted. Sim QPS=2667.0721. Mean native / sim =27.01. Native 200k vectors/1k queries; simulator 1024/8. Native allows affinity CPUs0–15 without explicit ANN OpenMP thread count. Simulator uses one core. Guest search time ~3 ms: timing granularity is a further concern.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 10
Two application metrics need new measurements
Native reference values are valid context; simulator smoke values are not matched tests.
SimCXL • BTP results • 4 Sep 2026
10
STREAM bandwidth
Native Triad: 21.71 GB/s
Mean of five reported best rates.
Sim Copy/Add: infinite rates.
Guest timer resolution ≈1 ms.
Reject the short-kernel rates.
Use a longer or tick-based ROI.
Pointer latency
Native: 60.92 ns/dereference
512 MiB buffer, five samples.
Sim: 7.437 ns/dereference
2 MiB buffer, one sample.
This is not a CXL-read latency.
Caches and sampling differ.
Notes: [Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 11
Latency is the strongest observed cost
What the current successful runs establish—and what they leave open
SimCXL • BTP results • 4 Sep 2026
11
Supported by measurements
CXL reads average ~300 ns;
P99 is near 600 ns.
Fabric and return contribute
about half the transaction time.
Brief admission backpressure
exists within mostly empty queues.
Still unmeasured
Incremental CXL slowdown
versus matched local memory.
Write and bidirectional limits;
endpoint bandwidth saturation.
Multi-endpoint balance and
application-specific phase costs.
Notes: [Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 12
Improve the experiment before tuning CXL
Recommended sequence • Separate CXL effects from measurement artifacts
SimCXL • BTP results • 4 Sep 2026
12
Priority
Change
What it resolves
1
Match local vs CXL runs
Isolates placement cost
2
Fix timers; mark useful work
Separates setup and kernels
3
Size data beyond relevant cache
Tests actual memory pressure
4
Set bandwidth; add read/write load
Tests saturation and directions
Notes: [Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 13
Test improvement hypotheses one at a time
Proposed experiments, not implemented gains • No speedup magnitude is established
SimCXL • BTP results • 4 Sep 2026
13
Modeled CXL performance
Sweep calibrated path latency;
measure application sensitivity.
Test more concurrent requests;
watch throughput and P99 together.
Vary queue capacity only with
evidence of sustained blocking.
Simulator execution cost
Run trace-on/off comparison
to measure logging overhead.
Aggregate metrics online while
preserving accounting semantics.
Fast-forward initialization with
a validated warmup and ROI.
Notes: Potential hardware/workload and simulator-host improvements are hypotheses from the inspected data and source. Reducing calibrated latency is a design exploration, not evidence of a valid current optimization. More outstanding requests can hide latency but raise queueing. Online aggregation and startup fast-forward need semantic validation and warmup. Avoid presenting host-time reductions as improved simulated CXL hardware.
[Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]

## Slide 14
Use matched runs to make the next claim
A reproducible comparison can turn descriptive measurements into a CXL result.
SimCXL • BTP results • 4 Sep 2026
14
Hold inputs, binaries, CPU, caches and measurement window fixed.
Change only memory placement: local DRAM ↔ CXL.
Then compare simulated workload time, throughput, read/write traffic,
latency tails and queue occupancy across repeated runs.
Sources: native campaign (1 Sep) + completed SimCXL phases (3 Sep).
Detailed source paths, definitions and qualifications are in the speaker notes.
Notes: [Sources]
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/comparison.json
/home/mahaswin/SimCXL/analysis/2026-09-04_native-vs-simcxl/README.md
Native data: /home/mahaswin/Downloads/BTP_CXL_Study/raw_data/{workload}/native_campaign/campaign_status.csv and referenced stdout_core_cache.log
Sim data: /home/mahaswin/SimCXL/results/2026-09-03_smoke-trial_065341/{workload}/cxl-workload-summary.json, workload.log, workload-config.json, stats.txt
Pointer report: /tmp/simcxl-recovered-20260903-170141/pointer_chase-cxl-metrics.json
[/Sources]